Freshmen Summer Internship Program 2013 / Assignment 3 / Avani Tanna, Alankar Kotwal / Electrical Subsystem

Section A: Drivetrain (Basic)

1)	No Name Functions and Description Applications / (i) Ball Bearing Type of a rolling element which uses balls to maintain separation between at least two bearing races. Transmits loads between one stationary and one rotating assembly through balls. / Reduces rotational friction and supports radial and axial loads. Contact between the wheels and axle. / (ii) Angular Contact Bearing The raceways here are displaced with respect to each other in the direction of the bearing axis. / This type of assembly accommodates radial and axial loads simultaneously. Contact between the wheels and axle. / (iii) Cylindrical Roller Bearing Rollers are in linear contact for the races. / They have high radial load capacity and are suitable for high speeds. Paper making machinery, / Wind turbines, / Gear boxes, / Electric motors, Motorcycles. / (iv) Tapered Roller Bearing Inner and outer raceways are sections of a cone, and rollers are also made with a taper. / It gives larger contact patch, and permits larger loads to be carried with spherical bearings. Car and vehicle wheel bearings. / Construction and mining equipment. / Axle systems, gear boxes, engine motors. / (v) Needle Roller Bearing Uses small cylindrical rollers. Used to reduce friction of a rotating surface. Have a large surface area that is in contact with the outer surfaces of the bearing and are much more compact. Rocket arm pivots, pumps, compressors. / Driveshafts of rear wheel drive vehicles.
2)	The gears used in the gearboxes of the EVo2 are helical gears. / No Gear Type Advantages Disadvantages Applications / (i) Spur Gear Easiest to design and manufacture. / Most efficient. / Cheap to purchase and maintain (teeth are straight rather than angular) More noise. / Slow speeds. / Cannot transfer power between non-parallel shafts. / Low load capacity. Gearboxes, in case of parallel shafts. / Load transfer. Changing rpm. / (ii) Helical Gears Silent operation. / Can transfer power between nonparallel shafts. / Can handle more load. Less efficiency. More cost. / Not easy to manufacture. Car gearbox. Machine tools. / (iii) Bevel Gears Makes it possible to change operating angle. / Differing number of teeth on each wheel allows mechanical advantage to be changed. One wheel of such a gear is designed to work only with its complementary, and must be precisely mounted. Differential drives. / Hand drills. / Rotorcraft.
3)	Advantages Disadvantages / High power density. / Large reductions possible in small volume. / Multiple kinematic combinations. / Pure torsional reactions. / Awesome power transmission efficiencies. / Very compact. / Torque capabilities greatly increased due to load distribution. / High rotational stiffness. / Greater stability. High bearing loads. / Constant lubrication requirements. / Inaccessibility. / Design complexity. / Derivation: / wp = Angular Velocity of the Planet Gears, rp = Radius of the Planet Gears. / ws = Angular Velocity of the Sun Gear, rs = Radius of the Sun Gear. / wa = Angular Velocity of the Annulus, R = Radius of the Annulus, with R = rs + rp. / 1) In case Sun Gear in kept fixed: We equalize the velocities of the gears which touch at the contact points. This gives: / %omega_a R = 2 %omega_p r_p giving a gear ratio of 2r_p over R or R over 2r_p / 2) In case Planet Gears are kept fixed: Equalizing the velocities we get: / %omega_s r_s=%omega_p r_p=%omega_a R giving a gear ratio of r_s over R or R over r_s / 3) In case Annulus is kept fixed: Equalizing the velocities we get: / 2r_s over r_p or r_p over 2r_s